## Slide 1
PAUCam mosaic 150 Mpixel
Scientific goal:
  Study the physics of the accelerating universe
  Method: precision photo-z (48 narrow band filters)
  Camera:
  18 CCDs (Hamamatsu Photonics, HPK), 2kx4k
  high quantum efficiency in near infrared
  there is not a filter wheel
  filters are automatically positioned above CCDs by means of
  14 mobile segmented filter trays operating in vacuum
  cryostat made of carbon fiber
  William Herschel Telescope (La Palma) in 2014
  also offered to the astronomical community as a facility
Juan De Vicente, CIEMAT (Madrid), Spain

## Slide 2
Back-End
Monsoon upgrade
135
Clocks
12
Videos
Control board
preamp boards (x18)
Focal plane
mix boards (x6)
2 complementary setups
Madrid
Barcelona
Readout Electronics
Front-End
CCD characterization
Curious dark cosmetic pattern in large exposures
Readout Noise: 5 e- rms @125 khz
Dark current: 1.1 e-/ h
Charg. Trans. Eff.: 0.999995
Python routines
IDL, C routines
L9 poster
Notes: 2