## Slide 1
Scientific Detector Conference 2017 - Baltimore
ESO AO Large Size CMOS Detector Controller
FPGA-based Real-Time Computer and Deformable Mirror Interface
Switching-mode Power Supply for Scientific Detectors
Javier Reyes
European Southern Observatory, ESO http://www.eso.org
jreyes@eso.org

## Slide 2
Precursor of the ESO LISA AO ELT camera
Based on Teledyne-e2v NGSD: 880x840, 700 fps
CMOS camera developed from scratch but compatible with ESO NGC universal controller standards and interfaces
NGSD
POSTER #1
Massive parallel architecture: 17600 ADCs, 10-bit
Key to stablish the technology of future LISA
ESO AO Large Size CMOS Detector Controller Prototype

## Slide 3
POSTER #1
NGSD camera prototype completed in 2016
Compact
Modular
Low-power
Based on Xilinx Kyntex-7 FPGA
Front-end
Bias/House keeping
Main board
Backplane
VHDL firmware
ESO AO Large Size CMOS Detector Controller Prototype
COTS FPGA module

## Slide 4
FPGA-based Real Time Computer and Deformable Mirror Interface
POSTER #2
Multi purpose board for VLTI NAOMI:
Adaptive Optics Module for Interferometry for ESO Very Large Telescope Interferometer (VLTI)
AO camera to RTC interface:
Corrective Optics to Alpao Deformable Mirror (DM241):
Alpao DM241

## Slide 5
FPGA-based Real Time Computer and Deformable Mirror Interface
POSTER #2
Based on Xilinx Virtex-5 FPGA
High-speed 2 Gbps fiber sFPDP connection to RTC
High-speed 2.5 Gbps fiber sFPDP connection to Corrective Optics computer
Support for deformable mirro multi stepping
Design fully tested
x 12 systems in production

## Slide 6
Low-noise Switching-Mode Power Supply for Scientific Detectors
POSTER #3
The architecture
EMI filter, 900 kHz notch filter
DC/DC converter
Fast peak detector
48 VDC input
Many outputs: 3.6 V, -10 V, +15 V, +25 V and +30 V.

## Slide 7
POSTER #3
Low-noise Switching-Mode Power Supply for Scientific Detectors

## Slide 8
Spectral content of the SMPS is no different
to the linear power supply
POSTER #3
Linear power supply
Switched-mode power supply
13 x 24 x 50 cm and about 18 Kg
¾ Moleskin notebook, twice its height and a couple of kilos
Low-noise Switching-Mode Power Supply for Scientific Detectors